## Slide 1: ONL
보라매NOC - IPC

## Slide 2: ONL
ONL (Open Network Linux)
- Open Network Linux is a Linux distribution for "bare metal" switches, that is, network forwarding devices built from commodity components.
- ONL uses ONIE to install onto on-board flash memory.
- Open Network Linux is a part of the Open Compute Project and is a component in a growing collection of open source and commercial projects.
ONIE ( Open Network Install Environment )
- Open Network Install Environment (ONIE) Project is a small operating system, pre-installed as firmware on bare metal network switches
- ONIE project enables a bare metal network switch ecosystem where end users can choose among different network operating systems
Notes: BEAM : Bogdan/Björn's Erlang Abstract Machine

## Slide 3: ONL
ONL 설치
ㅇ 리눅스에 NOS installer image 설치
linux:~$ sudo mkdir /mnt/usb
linux:~$ sudo mount /dev/sdd1 /mnt/usb
linux:~$ sudo cp ACME_XYZ1234_PowerPC_Installer.bin /mnt/usb/onie-installer
linux:~$ sudo umount /mnt/usb
ㅇ HTTP Server 설치
yum install apache
image-server:~$ sudo cp ACME_XYZ1234_PowerPC_Installer.bin /var/www
image-server:~$ ls -l /var/www
-rw-r--r-- 1 root root 17755 Jun 27 16:18 ACME_XYZ1234_PowerPC_Installer.bin
ONIE:/ #onie-nos-install http://10.0.1.251/home/path/to/your/build/images/cumulus-install-powerpc.bin
Notes: BEAM : Bogdan/Björn's Erlang Abstract Machine

## Slide 4: ONL
Current ONIE Hardware Status
Device | Vendor | Description | USB Support | DC Available | Reverse air-flow available | PXE Support | ONIE Provided | ONIE Sample in Lab | ONIE Certified | ONIE Certified Version | NOS - Open Source | NOS - Commercial | Configuration Management Tools
AS4600_54T | Accton | 48 Port 1GB with 4 SFP+ 10GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | Yes | 2014.08 | ONL | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
AS5600_52x | Accton | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes |  | NO | N/A | ONL | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
AS5610_52x | Accton | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | Yes | 2014.08 | ONL | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
AS5710_54x | Accton | 48 Port SFP+ 10GB with 6 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | NO | N/A | ONL | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
AS5712_54x | Accton | 48 Port SFP+ 10GB with 6 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | Yes | 2014.08 |  | BigSwitch, Cumulus, Pluribus | Ansible, Chef, Puppet, CFEngine
AS6700_32x | Accton | 20 QSFP+ 40GB Ports plus optional 6 or 12 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | NO | N/A | ONL | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
AS6701_32x | Accton | 20 QSFP+ 40GB Ports plus optional 6 or 12 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | Yes | 2014.08 |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
7448 | Agema | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes | UTSA | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
SNQ-60x0-320F | Alpha Networks | 32 Port QSFP+ 40GB | Yes | Yes | Yes | Yes | Yes | UTSA | NO | N/A |  |  | 
SNQ-60x0-486F | Alpha Networks | 48 Port SFP+ 10GB with 4 QSFP+ 40GB ports | Yes | Yes | Yes | Yes | Yes | UTSA | YES | 2014.08 |  |  | 
S4810-ON | Dell | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | No | Yes | Yes | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
S6000-ON | Dell | 32 Port QSFP+ 40GB | Yes | Yes | Yes | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
3200 | Penguin | 48 Port 1GB with 4 SFP+ 10GB Ports | Yes | Yes | Yes | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
3200XL | Penguin | 32 Port QSFP+ 40GB | Yes | Yes | Yes | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
4804x | Penguin | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | Yes | Yes | Yes | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
LB9A | Quanta | 48 Port 1GB with 4 SFP+ 10GB Ports | No | Yes | No | Yes | Yes | UTSA | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
LY2(R) | Quanta | 48 Port SFP+ 10GB with 4 QSFP+ 40GB Ports | No | Yes | No | Yes | Yes | UTSA | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
LY6 | Quanta | 32 Port QSFP+ 40GB | No | Yes | No | Yes | Yes |  | NO | N/A |  | BigSwitch, Cumulus | Ansible, Chef, Puppet, CFEngine
Notes: BEAM : Bogdan/Björn's Erlang Abstract Machine

## Slide 5: ONL
Current Network Operating System (NOS) List
Vendor | OS | Base | ONIE Compatible | Intel / Fulcrum | Broadcom | Mellanox
Alcatel-Lucent | Service Router Operating System (SROS) | VxWorks | NO | NO | YES | NO
Arista Networks | Extensible Operating System (EOS) | Fedora | NO | YES (7500 Series only) | YES | NO
Big Switch Networks | Switch Light | Debian | YES | NO | YES | NO
Broadcom | ICOS (FASTPATH) [1] |  | NO | NO | YES | NO
Brocade | IronWare |  | NO | NO | YES | NO
Cisco Systems | IOS |  | NO | NO | NO | NO
Cisco Systems | NXOS | MontaVista | NO | NO | YES | NO
Cisco Systems | iNXOS | MontaVista | NO | NO | YES | NO
Cisco Systems | IOS-XE |  | NO | NO | NO | NO
Cisco Systems | IOS-XR | QNX | NO | NO | NO | NO
Cumulus Networks | Cumulus Linux | Debian | YES | NO | YES | NO
Dell | Force 10 Operating System (FTOS) | NetBSD | NO | NO | YES | NO
Ericsson | SmartEdge Operating System (SEOS) | NetBSD | NO |  |  | 
Extreme | ExtremeXOS | BusyBox | NO | NO | YES | NO
Facebook | FBOSS |  | NO | NO | YES | NO
HP | Comware |  | NO | NO | YES | NO
HP | OpenSwitch | Yocto | NO | NO | YES | NO
Juniper | JunoOS | FreeBSD | NO | NO | YES | NO
OCP | ONL | Debian | YES | NO | YES | NO
Pica8 | PicOS | Debian | YES | NO | YES | NO
Pluribus Networks | Netvisor OS | Illumos/CentOS | NO | YES | YES | NO
Wind River / Intel | Intelligent Network Platform | vxWorks | NO | YES | NO | NO
Notes: BEAM : Bogdan/Björn's Erlang Abstract Machine